## Slide 1: High Speed Networks Need Proactive Congestion Control
Lavanya Jose, Lisa Yan, Nick McKeown, Sachin Katti
Stanford University
Mohammad Alizadeh
MIT
George Varghese
Microsoft Research

## Slide 2: At 100G, a typical flow lasts a few RTTs
1MB / 100 Gb/s = 80 µs

## Slide 3: Convergence times matter at 100G.

## Slide 4: Most congestion algorithms are slow
Adjust
Flow Rate
Measure Congestion
Adjust
Flow Rate
Measure Congestion
They don’t use any explicit info!

## Slide 5: Use explicit info., schedule flows faster
Link 1
30 Gb/s
Flow B
Flow A
flow | demand
A | 10 x 1.5KB
B | 5 x 1.5KB

## Slide 6: (1) Use explicit info.- allocate rates
Link 1
30 Gb/s
Flow B
Flow A
flow | demand
A | 10 x 1.5KB
B | 5 x 1.5KB
Flow B = 15Gb/s
Flow A = 15Gb/s
t = 0

## Slide 7: (2) Use explicit info.- schedule packets
Link 1
30 Gb/s
Flow A
flow | demand
A | 10 x 1.5KB
B | 10 x 1.5KB
1.5KB/ (30Gb/s) = 0.4us
0.4us A
0.8us B
1.2us A
1.6us B
Flow B

## Slide 8: Allocating rates v/s scheduling packets
Rate allocation easier to enforce at 100Gb/s
Notes: Though not clear how it compares to
distributed scheduling schemes.

## Slide 9: Distributed Rate Allocation
Distributed
Centralized
Timeslots/ packet
Rates at RTT timescales
X

## Slide 10: Distributed Rate Allocation (PERC)
flow | demand
A | ∞
B | ∞
Capacity at Link 1: 30G
So Fair Share Rate: 30G/2 = 15G
15 G
∞
∞
Link 1
30 G
Flow B
Flow A

## Slide 11: Bottleneck info. takes time to propagate
flow | demand
A | ∞
B | 
10 G
∞
Link 1
30 G
Link 2
10 G
Flow B
Flow A

## Slide 12: PERC converges fast
 | RCP | PERC
Median | 14 RTTs | 4 RTTs
Tail (99th) | 71 RTTs | 10 RTTs

## Slide 13: Open Questions

## Slide 14: Making PERC practical
Robust to control packet losses
Simple computation in switches

## Slide 15: Getting to max-min fair rates quickly
Fair Queuing?
Fastpass?
  reactive schemes (RCP etc.)
  explicit rate calculation (PERC etc.)

## Slide 16: What are “ideal rates”?
Max-min fair?
Fast distributed rate calculation schemes for other metrics?

## Slide 17: That’s all.

## Slide 18: Another dimension- Queue Sizes
Fastpass
Timeslot allocation
Zero-queues
TCP (AIMD)
Queue ~ BDP/sqrt(N)
Explicit Rate Calculation
RTT timescales
Transient Incast Queues
Fair Queuing